## Slide 1
IoT-Based Smart Electronics
Laboratory Safety and Asset
Monitoring System Using ESP32
USING: ESP32
MOHANAKRISHNAN S | KAWIN KUMAR P | ABINANDHAN A V | MANIISHANKAR V

## Slide 2
COMPONENTS
01
ESP32
HEART OF PROJECT
02
DHT11 SENSOR
TEMPERATURE & HUMIDITY
03
MQ-5 SENSOR
GAS DETECTION
04
FLAME SENSOR
FIRE DETECTION
05
HC-SR04
MOVEMENT DETECTION
06
LCD I2C
DISPLAY ADAPTER

## Slide 3
ESP32
01
ESP 32
H E A R T O F P R O J E C T

## Slide 4
THE HEART OF PROJECT
The ESP32 is a powerful dual-core microcontroller developed by Espressif Systems, featuring integrated 2.4 GHz Wi-Fi and Bluetooth/BLE. It is designed for IoT applications with a 32-bit Xtensa LX6 processor running at up to 240 MHz, 520 KB SRAM, and rich GPIO peripherals, programmed using the Arduino IDE.
Processor:
Tensilica Xtensa Dual-Core 32-bit LX6, 160/240 MHz
Operating Voltage:
3.3V (5V tolerant input pins)
Wi-Fi:
802.11 b/g/n 2.4 GHz
Bluetooth:
v4.2 BR/EDR & BLE
Flash Memory:
4 MB integrated
GPIO Pins:
34 programmable GPIO
ESP32 DevKit V1
Dual-Core MCU with Wi-Fi & BLE
GPIO 0–39 | ADC | PWM
I2C | SPI | UART | DAC
5V Input → 3.3V Logic
Arduino IDE Compatible
Board: ESP32 DEVKIT V1 DOIT

## Slide 5
DHT11 SENSOR
02
DHT 11
T E M P E R A T U R E M O N I T O R I N G

## Slide 6
DHT 11
The DHT11 is a low-cost, 3-5V digital temperature and humidity sensor designed for basic environmental monitoring. It provides temperature readings of 0-50°C and humidity from 20-80% RH. It uses a single-wire digital interface, making it easy to use with ESP32 via GPIO 4.
Key Specifications
Operating Voltage
3.3V to 5V
Temperature Range
0°C to 50°C (±2°C accuracy)
Humidity Range
20% to 90% RH (±5% accuracy)
Sampling Rate
1 Hz (once per second)
Interface
Single-bus digital signal
ESP32 GPIO
GPIO 4 (DATA pin)
Usage in Project:
• Monitors temperature & humidity in real time • LCD displays: T:29C H:65% • Data uploaded to ThingSpeak Field 1 & 2 • Connected to GPIO 4 of ESP32

## Slide 7
MQ-5 GAS SENSOR
03
MQ-5 SENSOR
G A S L E A K A G E D E T E C T I O N

## Slide 8
MQ-5 GAS SENSOR
The MQ-5 is a gas sensor that detects combustible gases including LPG, natural gas, methane, and smoke. It uses a heated metal-oxide semiconductor element whose resistance changes in the presence of target gases. Operates at 5V and provides analog output connected to GPIO 34 (ADC).
What It Detects
LPG • Methane
Smoke • Natural Gas
Combustible Vapors
Alert Threshold
Analog Value > 2500
Triggered instantly
Yellow LED + Buzzer ON
LCD Display
GAS LEAKAGE!
Value: [raw ADC]
Uploaded to ThingSpeak
Pin Connection
VCC → 5V
GND → GND
AO → GPIO 34

## Slide 9
FLAME SENSOR
04
FLAME SENSOR
F I R E D E T E C T I O N

## Slide 10
FLAME SENSOR & HC-SR04
FLAME SENSOR
Detects infrared radiation from a flame.
Output goes LOW when fire is detected.
Operating Voltage:
3.3V
GPIO:
GPIO 19 (Digital IN)
Alert:
Red LED + Buzzer
LCD:
FIRE ALERT! / CHECK LAB
ThingSpeak:
Field 5 = FIRE
HC-SR04 ULTRASONIC
Detects equipment movement using ultrasonic pulses. Measures distance; alerts when deviation > 10 cm from reference.
Range:
2 cm to 400 cm
TRIG:
GPIO 26
ECHO:
GPIO 27 (via divider)
Alert:
Blue LED + Buzzer
LCD:
EQUIP MOVED / D:XXcm

## Slide 11
I2C MODULE
05
I2C MODULE
D I S P L A Y A D A P T E R

## Slide 12
ALERT INDICATION LOGIC
CONDITION
LED INDICATOR
BUZZER
Normal / Safe
🟢 Green LED ON
OFF
Gas Leakage Detected
🟡 Yellow LED ON
ON
Fire Detected
🔴 Red LED ON
ON
Equipment Moved
🔵 Blue LED ON
ON
ALERT PRIORITY: 🔴 Fire → 🟡 Gas → 🔵 Movement → 🟢 Normal

## Slide 13
PIN CONNECTION DETAILS
COMPONENT
PIN
ESP32
DHT11
DATA
GPIO 4
MQ-5
AO (Analog Out)
GPIO 34
Flame Sensor
DO (Digital Out)
GPIO 19
HC-SR04
TRIG
GPIO 26
HC-SR04
ECHO
GPIO 27
LCD I2C
SDA
GPIO 21
COMPONENT
PIN
ESP32
LCD I2C
SCL
GPIO 22
Buzzer
+
GPIO 18
Green LED
Anode (220Ω)
GPIO 13
Yellow LED
Anode (220Ω)
GPIO 12
Red LED
Anode (220Ω)
GPIO 14
Blue LED
Anode (220Ω)
GPIO 25

## Slide 14
WORKING PRINCIPLE
1
Power ON:
System shows LAB SAFETY / SYSTEM on LCD and connects to Wi-Fi. Captures reference distance.
2
Sensor Reading:
DHT11, MQ-5, Flame Sensor, HC-SR04 are read continuously in the main loop every second.
3
Priority Alert Check:
Fire → Gas → Movement → Normal mode is evaluated in strict priority order each loop cycle.
4
Alert Output:
Color-coded LED activates, buzzer sounds, and LCD shows the specific alert with sensor value.
5
Cloud Upload:
Every 20 seconds, Temperature, Humidity, Gas, Distance & Alert Status sent to ThingSpeak.

## Slide 15
THINGSPEAK IoT DASHBOARD
Real-time sensor data is uploaded to the ThingSpeak cloud platform via Wi-Fi every 20 seconds, enabling remote monitoring from any mobile or laptop.
Field 1
Temperature (°C)
Field 2
Humidity (%)
Field 3
Gas Level (ADC)
Field 4
Distance (cm)
Field 5
Alert Status
DATA FLOW: Sensors → ESP32 → Wi-Fi → ThingSpeak → Mobile / Web Dashboard

## Slide 16
ADVANTAGES & APPLICATIONS
ADVANTAGES
APPLICATIONS
✓ Real-time multi-parameter monitoring simultaneously
✓ Priority-based alert ensures critical hazard shown first
✓ Color-coded LEDs allow instant visual alert identification
✓ Remote monitoring from anywhere via ThingSpeak cloud
✓ Low cost and scalable with additional sensors
▶ Electronics & Computer Science lab safety
▶ Industrial gas and fire hazard monitoring
▶ Asset tracking in research labs
▶ Smart building environmental automation
▶ IoT embedded systems education demo

## Slide 17
CONCLUSION
The IoT-Based Smart Electronics Laboratory Safety and Asset Monitoring System successfully demonstrates the integration of multiple sensors with an ESP32 microcontroller and IoT cloud platform.
This project demonstrates how multiple sensors can be integrated with a microcontroller and cloud platform to build an efficient and smart monitoring system. It is scalable and can be enhanced with additional sensors and features in the future.
THANK YOU
MOHANAKRISHNAN S KAWINKUMAR P ABINANDHAN A V MANIISHANKAR V